## Slide 1
3.28 MRM_COMM_CHECK_REQUEST (0xFFFE)
API: MRM_API
Message type: REQUEST (Host)
Corresponding Message type: MRM_COMM_CHECK_CONFIRM (Radio)
Purpose: This is request message sent by the Host to MRM asking for a communications check to be performed which involves send-repeat pattern to ensure data is being correctly encoded/transmitted and received/decoded.
Packet Definition
# | Parameter | Type | Definition
0 | MRM_COMM_CHECK_REQUEST (0xFFFE) | UINT16 | Message type
1 | Message ID | UINT16 | A tracking number used to associate Host REQUEST messages to MRM CONFIRM messages.
2 | Unsigned 8-bit integer check value | UINT8 | Test value that will be repeated back to Host by MRM in MRM_COMM_CHECK_CONFIRM.
3 | Unsigned 16-bit integer check value | UINT16 | Test value that will be repeated back to Host by MRM in MRM_COMM_CHECK_CONFIRM.
4 | Unsigned 32-bit integer check value | UINT32 | Test value that will be repeated back to Host by MRM in MRM_COMM_CHECK_CONFIRM.
5 | Signed 8-bit integer check value | INT8 | Test value that will be repeated back to Host by MRM in MRM_COMM_CHECK_CONFIRM.
6 | Signed 16-bit integer check value | INT16 | Test value that will be repeated back to Host by MRM in MRM_COMM_CHECK_CONFIRM.
7 | Signed 32-bit integer check value | INT32 | Test value that will be repeated back to Host by MRM in MRM_COMM_CHECK_CONFIRM.

## Slide 2
3.29 MRM_COMM_CHECK_CONFIRM (0xFFFF)
API: MRM_API
Message type: CONFIRM (Radio)
Corresponding Message type: MRM_COMM_CHECK_REQUEST (Host)
Purpose: This is the message sent by the MRM in response to a MRM_COMM_CHECK_REQUEST from the Host. It repeats the information provided in the request along with additional information.
Packet Definition
# | Parameter | Type | Definition
0 | MRM_COMM_CHECK_CONFIRM (0xFFFF) | UINT16 | Message type
1 | Message ID | UINT16 | A tracking number used to associate Host REQUEST messages to MRM CONFIRM messages.
2 | Unsigned 8-bit integer check value | UINT8 | Test value provided in MRM_COMM_CHECK_REQUEST repeated back to Host by MRM.
3 | Unsigned 16-bit integer check value | UINT16 | Test value provided in MRM_COMM_CHECK_REQUEST repeated back to Host by MRM.
4 | Unsigned 32-bit integer check value | UINT32 | Test value provided in MRM_COMM_CHECK_REQUEST repeated back to Host by MRM.
5 | Signed 8-bit integer check value | INT8 | Test value provided in MRM_COMM_CHECK_REQUEST repeated back to Host by MRM.
6 | Signed 16-bit integer check value | INT16 | Test value provided in MRM_COMM_CHECK_REQUEST repeated back to Host by MRM.
7 | Signed 32-bit integer check value | INT32 | Test value provided in MRM_COMM_CHECK_REQUEST repeated back to Host by MRM.
8 | Datetime string | CHAR[15] | Unicode string representing datetime at which the request was received and parsed. Format is %Y%m%dT%H%M%S, https://docs.python.org/3/library/datetime.html#strftime-and-strptime-format-codes.
9 | Status | UINT32 | 0 = Successful. For error codes see Table 3-1 at the end of this section.